KFS x86 projects
# Projects objectives
## KFS-1
The objective of KFS-1 is to write a bootable kernel that handles a mini VGA driver and so displays some text on the screen.
## KFS-1
Using the prerequisites of the last project, the aim of KFS-2 is to split the memory in dedicated and protected areas called segment that will be used for particular purposes by the kernel and user processes.
# Answering the problematic
## KFS-1
We write code that we want to be executed. Remember that you are ring 0, so no abstract layers and libraries are available. (like memory allocation and so on...)
Our code must be compiled without any dependencies since no existing libraries header and code s running nor stored on our machine.
To make a kernel bootable, we must respect some approved rules. The signature of the kernel, which will allow the bootloader (GRUB here) to detect our binary as a kernel is called the multiboot header.
We write sources and linker file to perform the requested task. An ASM file let us define a special section called the multiboot section, that contains particular values used by the bootloader at load time to bootstrap the kernel (A checksum, memory map request, requested physical address for loading the kernel code segment, etc...). It allows the kernel to be recognize as it is, but it will also ask the bootloader some informations, the multiboot header can hold various requests.
- For that we write an ASM file in which we add a multiboot header in a dedicated section. Since we write our kernel in C, we also need to create a space in memory for a stack to be used by our C functions. For that we declare 2 symbols spaced by the size in byte we want for our stack, and we load the address of the uppermost symbol in the stack pointer register (the stack grows downward).
- In the C files, we use the I/O port address to locate with the controller registers of the screen on the I/O bus, here the VGA controller. Those addresses are assigned and resolved by the BIOS at power off. The components being integrated in the motherboard, these addresses do not change. Once we know the address and location of the registers, we can use them to control and communicate the HW using the control and data registers. For the cursor for example. We know the address of the VGA buffer. The buffer is made of 50x80 short. The lower byte being for the ASCII character and the uppermost byte being for the font and background color.
But the multiboot header has to be located in the first 8Ko of the final executable to ensure being read by GRUB. For that, we write a linker script that will order the sections in the file segments to make sure that the multiboot section that contains the multiboot header is at the beginning of the file.
Our mini VGA driver being done, and all prerequisites for the kernel being written, we must link our sources together. For that we write the linker and put in that we want the multiboot section being the first in the text segment. That sections should be aligned on 4K, we also say that we want our sections to be place at an offset of 2Mo (To let space for bootloader it self and other stuff apparently). And of course we specify our entry point, here the _start function.
Once the executable is created, we build an image of it containing grub. For that we used :
$> grub-mkrescue -o $(OS_IMAGE_NAME) $(ISO_DIR) --compress=gz
instead of recompiling GRUB, which is annoying really. But be careful, this command will take parts of GRUB present in your current system, so do it on a x86 platform..
You’re done, you can now test it with qemu.
NOTE: The GRUB bootloader interprets ELF format
Refs :
- multiboot documentation
- OSdev bare bones (Compile C in ASM, Assemble ASM to object code, Link object code to ELF binary)
- IN instruction
- I/O Ports I/O range I/O port address I/O port addresses
- Linker script
## KFS-2
In KFS-1, we wrote sources and linker file to perform the requested task. An ASM file let us define a special section called the multiboot section, that contains particular valued used by the bootloader at load time to bootstrap the kernel. It allows the kernel to be recognize as it is, but it will also ask the bootloader some informations, the multiboot header can hold various requests.
Refs : multiboot documentation
# Documentation
## Basics : !! REWORD!!
Bootloader: A kernel / OS is loaded in memory by the bootloader. The bootloader is a piece of binary software that is located at a known by the BIOS position on the disk, and which will be loaded first. Its main role is to locate the kernel on disk , and load it into memory at the desired place, then to "disappear". It has other functions like checking HW drivers and stuff for OS compatibility, etc... In our case, we will use the GRUB bootloader that understand the ELF binary format, and will load specific program headers or segments according the the binary format and content. But it also understand raw binary.
MBR: The bootloader used to be located on the Master Boot Record (MBR), which is the first adressable sector of the hard drive. The MBR contains the patrition table of the hard drive, and the boot strap routine that launches the OS (or a more recent bootloder).
But the MBR is limited to 2,2 To disks and 4 partitions. A more recent techno is GPT (GUID Parition Table).
The MBR used to be parsed and its routine executed by the BIOS ; now, the GPT is loaded by UEFI. GPT might handle more partitions and faster boots.
Important thing to note is that GPT must be compatible with the MBR and the legacy BIOS, so the first logical bloc 0 must remains to the MBR, with the logical bloc 1 is used by GPT. To be continued...
Multibooting & Multiboot header: Multibooting is the ability of a single bootloader to load various kernel. For that, kernels need a multiboot header, which is a data structure in its image which provides infos to the Multiboot-compliant bootloaders (i.e GRUB), about how and where to load the kernel image.
for example, Grub may provide the kernel with a memory map when it starts, but it would be a waste of time if the kernel does not require it. the Flags indication in the multiboot header is used to specify whether or not the kernel loaded expect a map. or oher infos, the magic number allows Grub to find the location of the multiboot header, it is the signature of the multiboot hdr.
Why and how to create a mutiboot hdr and data structure: https://www.gnu.org/software/grub/manual/multiboot/html_node/OS-image-format.html#OS-image-format
When a kernel is loaded, it does not have a stack (meaning that when C compiled code will manipulate addresses supposed to be above or relative to the program addresses, it might erase / step out the scope of PM (Physical memory), particularely since virtual memory is not used yet), netiher virtual memorynor other features that will be provided by the kernel itself to further sub processes/
the bootloader, grub here, needs to know how to load the kernel :
 - Where in PM to place the code. data. and other segments of the ELF
 - What flags or protection to use / give to the kernal, etc...
. . .
Multiboot has a standard which describes infos the bootloader will read to load the kernel . Values are in form o magic numbers and defined by the standard. Those values represent the multiboot header. Since Grub do parse ELF file format. it understands sections & segments.
a special section called .mutliboot that contains the multiboot header values will be placed in the in the first 8ko of the OS image file and must be aligned on 32bits / 4bytes. It is the multiboot header that mark the program has a kernel.

So kernal has 2 stages: low and high level. Low level will set up environnment, section to segment stack and set stack pointer to the start of the stack location and other hardware initalization. Then it will call the high level function that do execute what we want the kernel to do.

In low level kernel, memory management like paging and segmentation (which include Global descriptor table for segment addresses and stuffs ) , interruption tables to interract with hardware like keyborad or mouth, or global C++ constructors and other stuffs are done here.
refs:
https://wiki.osdev.org/Inline_Assembly
https://wiki.osdev.org/Multiboot
https://wiki.osdev.org/Bare_Bones
https://blogs.bu.edu/md/2011/11/15/the-dark-art-of-linker-scripts/

https://dev.to/frosnerd/writing-my-own-vga-driver-22nn
1. Communicate with the screen without BIOS interrupt:
Using VGA standard to write on the screen, we need to write a small VGA driver.
a. Reading and writing cursor position: device port available at memory location 0x3d4 and 0x3d5. We must use port devices instruction in & out.
## Memory management x86
The memory mapping in x86 works with segments (and optionally pagination too). Inside a binary file, content is organized in segments too, with particular protection and access rights. In a program file aspect, a logical address is the address of instruction and data inside a binary file itself, offsets within the file and from a program header. But once projected in memory, the upper part of the address is replaced by the address of the corresponding memory segment (code or data). (In 64bits segmentation is obsolete and the upper part of the address is a virtual page address, segment registers content is used for other purposes).
We have to understand how the logical and linear address spaces are used.
### Logical addresses
A logical address is composed of a segment selector (selector being a index in a table of descriptors, itself containing the base address of the segment) and an offset within this segment. At the file step, the logical address contains only an offset within the file or the file segment, in order to be completed at execution time to add the memory segment address in which we want to store the data / instruction. The offset is important because it allows relative instructions / data accesses.

### Linear addresses
Without pagination, which add another level of abstraction between virtual and physical memory, the linear address space is equivalent of the physical address space. (And so without pagination, virtual address space can not exceed the physical memory space)
A linear address is the address of the symbol in memory. And the construction of this address is a full process itself.
To allow a program to be placed in memory, and passing from logical addresses to linear addresses, the kernel has to know the base address of each segments, maintain tables and structures of the virtual to physical memory mapping and also to which belongs a
TO FINISH
## Principle of segmentation
### Segments
### Segments descriptor
### Segments selector
### Segment registers
### Pagination and segmentation
### GDT
### LDT
### IDT
### TSS
To allow multitasking, 80386 set up multiple data structures. However no special instructions are used ; instead, the system act differently according to the data structure handled.
The data structures and registers responsible for supporting multitasking are:
- Task state segment (TSS)
- Task state segment Descriptor
- Task registers
- Task gate descriptor.

## Control registers
### GDTRegister
### LDTRegister
### IDTRegister
## In practical
### Setting up a GDT
#### What to Put In a GDT
SYSENTER / SYSEXIT
#### How to Set Up The GDT
- Disable Interrupts
- Filling the tables
- Advising the CPU about its location
- Real mode
GDT and GDT_end are assumed to be symbols in the current data segment.
### Setting up an LDT
### Setting up an IDT